## Slide 1
Grzegorz Bury1, Krzysztof Sośnica1, Radosław Zajdel1, Dariusz Strugarek1, Urs Hugentobler2
Global reference frame realization onboard GNSS satellites
1 Institute of Geodesy and Geoinformatics, Wrocław University of Environmental and Life Sciences, Grunwaldzka 53, 50-357 Wroclaw, Poland
2 Institute for Astronomical and Physical Geodesy, Technical University of Munich, 80333, Munich, Germany

## Slide 2
Subject of this study
Geodetic Datum Realization using co-location onboard GNSS
  What is the best strategy for constraining GNSS and SLR network?
  How should we handle the SLR systematic errors (range biases)?
  How well can we determine the linkage between SLR and GNSS in space?

## Slide 3
ITRF
GNSS: double-difference network solution
SLR: zero-difference network solution
SLR:
Geocenter is not explicitely estimated thus the SLR requires NNR, whereas GNSS network requires NNT+NNR constaint.
Local Tie

## Slide 4: Integration of SLR and GNSS onboard Galileo (GNSS)
APC – GNSS antenna phase center
APR – GNSS antenna reference point
TRP – SLR telescope reference point
LRA – laser retroreflector array
C-o-M – GNSS satellite center-of-mass.
LRA for SLR
GNSS
antenna

## Slide 5
Space ties
GNSS: double-difference network solution
SLR: zero-difference network solution
SLR:
NNT+NNR needed for SLR stations? NNT+NNR needed for GNSS stations?
Do the space ties transfer the network orientation and translation?
NNT+NNR needed for both, SLR and GNSS stations?
Space Tie

## Slide 6: GNSS and SLR network
SLR stations
GNSS stations

## Slide 7: Different approaches to the datum realization
 | Solution | GNSS | SLR | GCC
Constraints on GNSS network | G1 | NNT/NNR | NO/NO | +
Constraints on GNSS+SLR networks | C1 | NNT/NNR | NNT/NNR | +
 | C2 | NNR | NNT | -
 | C3 | NNR | NNR | -
 | C4 | NNR/NNT | NNT | +
 | C5 | NNR | NNT/NNR | +
Cannot realize SLR network (not bad for SLR stations!)
GCC in GNSS network
Similar to G1 – orientation for the SLR network cannot be transfered via GNSS satellites (lack of NNR condition)
Very poor GCC and CRD
Best for GNSS and SLR

## Slide 8: Quality of station coordinates
GNSS
SLR
Homogeneity of GNSS network
C1, C4, G1 – NNT/NNR + GCC
C2, C3– NNR – GCC
C5 – NNR + GCC
Inhomogeneity of SLR network
Best performing stations: 7090, 7810, 7941, 8834
C1 (NNT/NNR) and G1(No constraints!) the best for SLR station coordinates

## Slide 9: 3D local tie (1/2)
Local ground measurements
GNSS-SLR stations distance based on the a priori ITRF2014/SLRF2014
Local tie calculated based on GNSS and SLR observations
SLR station
GNSS station
Local tie

## Slide 10: 3D local tie (2/2)
Local ground measurements
GNSS-SLR stations distance based on the a priori ITRF2014/SLRF2014
Local tie calculated based on GNSS and SLR observations
SLR station
GNSS station
Local tie
Strength of the 1-day connection: 40-50 mm
Long-term agreement: 3-4 mm

## Slide 11: Difference between space and local ties

## Slide 12: Difference between space and local ties

## Slide 13
Summary
The best strategy for the datum realization aiming is consistent imposing of NNT+NNR constraints on GNSS and SLR sites
The strength of the connection onboard GNSS satellites is 40–50 mm for the1-day solutions for individual stations, whereas the mean values based on long time series agree to 3–4 mm with local tie measurements.
SLR range biases considering the LAGEOS-based station coordinates improve the consistency with the in situ local ties (Up).

## Slide 14: Thank you for your attention
Bury G, Sośnica K, Zajdel R, Strugarek D, Hugentobler U (2021) Determination of precise Galileo orbits using combined GNSS and SLR observations. GPS Solut 25(1):11. https://doi.org/10.1007/s10291-020-01045-3
Bury G, Sośnica K, Zajdel R, Strugarek D (2022) GLONASS precise orbit determination with identification of malfunctioning spacecraft. GPS Solut 26(2):36. https://doi.org/10.1007/s10291-021-01221-z
Find more details in:
Dr Grzegorz Bury
grzegorz.bury@upwr.edu.pl
More scientific content:
https://www.researchgate.net/profile/Grzegorz-Bury
https://orcid.org/0000-0002-5816-410X
Bury G, Sośnica K, Zajdel R, Strugarek D, Hugentobler U (2021) Geodetic Datum Realization Using SLR‐GNSS Co‐Location Onboard Galileo and GLONASS. JGR Solid Earth 126(10). https://doi.org/10.1029/2021JB022211